## Slide 1: Head Controlled Human Interface Device for Persons with Limited Hand Movement
Georgia Institute of Technology
School of Electrical and Computer Engineering
ECE 4007
Dr. Arthur Koblasz
Augmented Comm Group
Roberto Pereira
Seth Stewart
Jarius Tillman
Sarvagya Vaish
March 14, 2013

## Slide 2: Overview
Prototype system to enable patients with spinal cord injury and limited hand mobility, to interface with a computer.
Estimated Cost
Component | Cost | 
9 DOF Sensor Stick (IMU) | $100.00 | 
Arduino Due | $50.00 | 
Wires and Headers | $15.00 | 
Optical Flow, Mouse Sensor (OFS) | $0.00 | (donated)
Custom PCB | $0.00 | (donated)
3D Printed Plastic Housing | $0.00 | (donated)
Total Cost | $165.00 | 

## Slide 3: Technical Objectives
Translate head pitch and yaw movements to computer cursor displacement
Translate eyebrow raises and winces to left and right clicks, respectively

## Slide 4: Design Objectives
Integrate all components into a small wearable device

## Slide 5: Modified Hardware Block Diagram

## Slide 6: Modified Control Flowchart
Sensor data processing moved from Arduino (on-chip) to the host computer

## Slide 7: Current Status – Head Tracking
Purchased IMU sensor from Sparkfun
Used Arduino program to convert head movements to digital signals
Created Processing program to translate digital signals to cursor movements
Demo
SparkFun - $100

## Slide 8: Head Tracking Algorithm
Adjustment Rate
New Cursor
Position
Old Cursor
Position
Sensor displacement from Neutral position
(x, y)
Quadratic sum of differences
At every time step -
The neutral position moves towards the cursor

## Slide 9: OFS Electronics
Optical Flow Sensor donated by PixArt Imaging
Created a custom PCB for holding the sensor
OFS
IR LED
Header Pins for Wires
PCB Design

## Slide 10: OFS Hardware
Iterating over 3D printed mounting to test PCB, lens, and OFS

## Slide 11: Current Issues
OFS recognizes skin movement only when placed at a particular distance from the skin
Need to create an adjustable mounting system
Alternatives
Bite-switch
Recognize nods and head shakes using IMU
Bite-switch

## Slide 12: Project Schedule
Activity | Date
1. Continue working with OFS | March 24
2. Find and implement OFS alternative (in case point 1 fails) | April 7
3. Fabricate mounting for sensors | April 14
4. Test and remove bugs | April 21
5. Senior Design Expo | April 25